## Slide 1: DTS205TC High Performance Computing
Lecture 4 Network 2
Di Zhang, Spring 2024

## Slide 2: Objectives of today's lesson

## Slide 3: Three networking methods to know
Analogy between WAN and postal network
  Both sender and receiver must have an address
  Hierarchical Address/Zip Code
  Collect messages from streets and cities to provinces, and then disperse to cities and streets
Type | Device | Purpose | Scope | Entity | Address | Delivery Method
Wide Area Network | Router | Connected to Internet | Global | Host with an IP address | IP | Forward along network
Local Area Network | Switch | Company/School | Building | Node with a net card | MAC | Forward along network
Local Area Network | Hub | Family | Home | Node with a net card | MAC | Broadcast

## Slide 7: Three networking methods to know
Analogy between LAN by switch and Mailbox
  The receiving and sending parties only need to have their names (assuming there are no duplicate names)
  Address format: only one level
  Forwarding, usually up to two levels
Type | Device | Purpose | Scope | Entity | Address | Delivery Method
Wide Area Network | Router | Connected to Internet | Global | Host with an IP address | IP | Forward along network
Local Area Network | Switch | Company/School | Building | Node with a net card | MAC | Forward along network
Local Area Network | Hub | Family | Home | Node with a net card | MAC | Broadcast

## Slide 8: Three networking methods to know
Analogy between LAN by hub and loudspeaker
  Broadcast by name without any forwarding
Type | Device | Purpose | Scope | Entity | Address | Delivery Method
Wide Area Network | Router | Connected to Internet | Global | Host with an IP address | IP | Forward along network
Local Area Network | Switch | Company/School | Building | Node with a net card | MAC | Forward along network
Local Area Network | Hub | Family | Home | Node with a net card | MAC | Broadcast

## Slide 9: Section
Network layer

## Slide 10: How to design an Internet?
The Inter-net is a global network that comprises many voluntarily interconnected autonomous networks.
Key: TCP/IP Protocol
the first internetworked connection

## Slide 11: Design goals
Functionality
  TCP: connection, connectionless
  IP: forwarding and routing
  ICMP: control
  IGMP: multicast

## Slide 12: Design goals
Non-Functionality (DFX)
  Simplicity：
    Only has necessary functions for communication
    Does not involve hardware, application

## Slide 13: Design goals
  Extensibility
    In theory, TCP and IP can be independent of each other

## Slide 14: Design goals
  Scalability：
    Support billions of devices
  Performance
    Fast Processing
Visualization of Internet routing paths

## Slide 15: Network layer: forwarding and routing
Differences from postal mail: Digitization
    The address and letter format must be standardized Large number of messages and high speed required (80Tbps for a typical router) Address allocation order, which does not imply a geographic hierarchy The address changes dynamically Routing paths are diverse and dynamic

## Slide 16: IP Datagram format
ver
length
32 bits
payload data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
destination IP address
options (if any)
IP protocol version number
header length(bytes)
upper layer protocol (e.g., TCP or UDP)
total datagram
length (bytes)
“type” of service:
diffserv (0:5)
ECN (6:7)
fragmentation/
reassembly
TTL: remaining max hops
(decremented at each router)
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead for TCP+IP
overhead
e.g., timestamp, record route taken
32-bit source IP address
32-bit destination IP address
header checksum
Maximum length: 64K bytes
Typically: 1500 bytes or less

## Slide 17: Q:
Why not use XML as the format?

## Slide 18: Forwarding table

## Slide 19: Hierarchical addressing: route aggregation

## Slide 20: Implementation of router
Knowing the above principle, you can even implement a router with a PC However, as mentioned in Lec. 1, the general von Neumann architecture has slower performance

## Slide 21: Routers in reality
Note that the wireless router in daily life is actually a link-layer device, not the router mentioned here

## Slide 22: Routers in reality
Input Port: Parses packets and determines the forwarding destination Switch fabric：Message transmission
Output Port: Packet encapsulation

## Slide 23: Switching fabrics
Network inside Network
bus
memory
memory
interconnection
network
Mechanical Crossbar

## Slide 24: Generation of forwarding table
By exchanging information between routers By a centralized controller
The forwarding table in each router must provide a forwarding destination for all IP addresses; That is, the forwarding table provides a holistic picture of the Internet's connectivity based on a local perspective

## Slide 25: Section
Link layer

## Slide 26: The functionality of the Link layer
There are three phases:
  Take responsibility that IP protocol leave blank, but needed to drive the hardware
    Error detection, retransmission, etc.
  Multiple nodes share a link
    Provide a simple, inexpensive way
  Link layer switches
    Straightforward and easy to use

## Slide 27: Ethernet datagram
Synchronization, sending and receiving addresses, verification

## Slide 28: Multiple access links
broadcast (shared wire or medium)
  old-fashioned Ethernet
shared wire (e.g.,
cabled Ethernet)
shared radio: WiFi
shared radio: satellite
humans at a cocktail party
(shared air, acoustical)
shared radio: 4G/5G

## Slide 29: CSMA/CD
Carrier Sense Multiple Access with Collision Detection
Transfer -> Detect Collision -> Wait a random period -> retry

## Slide 30: Link layer switch
Forwarding table
  Strictly matches the destination address one by one Self-learning capability, no configuration required

## Slide 31: Comparison of devices
Comparison of the typical features of popular interconnection devices

## Slide 32: Topology of usual networks
Topology
  describes how elements of a set relate spatially to each other (wiki)
Star: The simplest structure (* -- linked by a switch with an internal bus)
Tree: Direct contact between two leaves will be slow. For general needs, such as surfing Web, direct contact is rarely required, but it is not for HPC.
Switch*
Switch
Switch
Switch

## Slide 33: Other possible network structures
Balance between cost and performance:
  More connections always make communication faster
  The higher the number of connections, the higher the cost
Obviously, some structures look more “reasonable” and “connected” than others
  How to quantify this concept?
Linear
Loop
2-D mesh
2-D wraparound mesh
3-D mesh
Fully Connected
Fat Tree